Demonstration of Grab Mercury Sample Collection Using Clean Hands/Dirty Hands Technique

# January 15, 2003

Susan Copeland

Bobby Hanna

Stephanie Scheringer

City of Gastonia

Wastewater Treatment Division

## Preliminary Preparation

- Laboratory cleans fluoropolymer sample collection bottles and double bags them in zip type bags.

- Sample collectors clean and bag sampling equipment.

- Sample collectors prepare sampling packages.

### Sampling Packages

- Designated clean cooler(s) containing:

- Cleaned and bagged sample tubing

- Zip bags with dust masks and non-talc Class 10 clean gloves

- Plastic sheet for ground cover

- Sample bottles (from laboratory)

- Tyvek suits- (optional)

- Peristaltic pump with easy load head.  Extension cord, if necessary.

- Waste bucket.

- Sample storage cooler.

- Carboy with DI water for Field Reagent Blank, if necessary.

### Site Preparation

- Upon arrival at the sampling site, the sample collectors unload equipment and prepare for sample collection.

- Anything covering the sample site, such as a grate or manhole, is removed and set aside.

- Plastic is laid out for ground cover, with coolers on the ends to secure.

- Set up peristaltic pump.

- Clean Hands (CH) and Dirty Hands (DH) sample collectors get into position.

- CH and DH wait ten minutes before beginning sample collection to allow the sampling environment to stabilize.

### Sample Collection

### A.  Field Reagent Blank

- DH opens the cooler and removes plastic bags containing gloves and masks.

- CH and DH put on dust masks first and then gloves.

- DH removes the lid from the carboy containing DI water for the FRB.

- DH removes the bag containing the sample tubing from the cooler.

- DH opens the bag.

- CH removes the tubing and does not allow the tubing to touch anything.

- CH removes the protective covering from the inlet side of the tubing.

- CH lowers the weighted end of the tubing into the carboy.

- Once the inlet end of the tubing enters the carboy, DH holds the tubing.

- DH inserts the flexible portion of the tubing into the peristaltic pump, while CH holds the discharge end of the tubing, protecting it from contamination.

- CH removes the protective covering from the discharge end of the tubing and holds it over the purge container.

- CH tells DH to turn the pump on.

- CH holds the sample line over a purge container while purging for a minimum of five minutes.

- After purging, CH tells DH to turn the pump off.

- DH opens the cooler containing the double-bagged sample bottle.

- DH opens the outside bag and does not touch the inside bag.

- CH removes the inside bag (containing the sample bottle).

- CH opens the bag and sample bottle.

- CH holds the discharge end of the tubing over the sample bottle and tells DH to turn the pump on.

- Once the sample bottle is filled, CH tells DH to turn the pump off.

- CH tightly caps the sample bottle and reseals it in the inside plastic bag.

- DH holds the outside bag open and CH places the inside bag, with the sample, into it.

- DH reseals the outside bag.

- The sample is then placed into the storage cooler.

##### B.  Sample Collection

- CH removes the inlet end of the tubing from the carboy of DI water and places it into the sample location.

- DH holds the tubing and makes sure that the inlet end and sides of the tubing do not contact anything.

- Sampling proceeds as in A12 – A24 above.

- Sampling site is cleaned and the sample is transported to the lab.

# Text boxes

Dirty Hands

Teflon Tubing

Clean Hands

Peristaltic Pump

## Grate

Sample Collection Bottle

WWTP Plant Effluent

City of Gastonia WWTP Effluent Sample Collection