Chapter 10

OTHER PROJECT TYPES

(Note—this section is to be interpreted based on current guidance for the HMA program as periodically updated by FEMA)

Storm Water Projects:

Projects to lessen the frequency or severity of flooding and decrease predicted flood damages, such as the installation or modification of culverts and stormwater management activities such as creating retention and detention basins. These projects must not duplicate the flood prevention activities of other Federal agencies and may not constitute a section of a larger flood control system.

For RFC and SRL, at least 50 percent of the structures directly benefiting from this mitigation activity must be NFIP-insured. In addition, these projects must primarily benefit RFC or SRL structures, respectively. Documentation must be provided in the sub-application to satisfy this requirement.

Retrofitting:

Structural Retrofitting of Existing Buildings – Modifications to the structural elements of a building to reduce or eliminate the risk of future damage and to protect inhabitants. The structural elements of a building that are essential to protect in order to prevent damage include foundations, load-bearing walls, beams, columns, building envelope, structural floors and roofs, and the connections between these elements.

Non-structural Retrofitting of Existing Buildings and Facilities – Modifications to the non-structural elements of a building or facility to reduce or eliminate the risk of future damage and to protect inhabitants. Non-structural retrofits may include bracing of building contents to prevent earthquake damage or the elevation of heating and ventilation systems.

Infrastructure Retrofit – Measures to reduce risk to existing utility systems, roads, and bridges.

Demo-rebuild:

Demo-rebuild refers to the demolition of an existing structure situated in a flood-hazard area and replacing it with a new structure of similar size and value that is built to current code and flood damage prevention ordinance standards. It is anticipated that demo-rebuild will be an eligible project type for the National Flood Hazard Mitigation Program authorized by the Biggert-Waters NFIP Reform Bill signed into law July 6, 2012. Guidance on this project type will be added to this SOP when such guidance is published by FEMA.

Generators:

Permanently installing generators or generator hook-ups are not generally eligible as stand-alone activities but are eligible only when included as a functional component of eligible mitigation activities. Under PDM, for a permanently installed generator and/or related equipment purchases (e.g., generator hook-ups) to be eligible, the generator has to be directly related to the hazards being mitigated and part of a project. However, the 5% Initiative allows for the stand-alone purchase of permanently installed generators. This initiative is used when mitigation activities are difficult to evaluate using FEMA-approved BCA methodologies. Up to 5 percent of the total HMGP funds may be set aside by the Grantee to pay for such activities. Effective December 2012, FEMA has ruled that stand-alone generators ARE eligible under the Hazard Mitigation Grant Program project fund provided a positive benefit/cost ratio can be demonstrated.

Hazard Mitigation Planning:

Mitigation plans are the foundation for effective hazard mitigation. A mitigation plan is a demonstration of the commitment to reduce risks from natural hazards and serves as a strategic guide for decision makers as they commit resources.

Planning activities funded under HMA are designed to develop State, Tribal, and local mitigation plans that meet the planning requirements outlined in 44 CFR Part 201. A mitigation planning sub-grant award must result in a mitigation plan adopted by the jurisdiction(s) and approved by FEMA prior to the end of the Period of Performance (POP).